## Slide 1: Demand Response Event Analysis: 6/14/22 Heat Wave
Customer Performance, Baseline Comparison, and Financial Results
Ruiyan Huang
Mar 2, 2026

## Slide 2
Event Overview & Methodology
June 14, 2022 | 2:00–6:00 PM Severe Midwest heat wave High demand + low wind output Emergency DR dispatch (first in ~6 months)
DATA
5 customer sites
15-min interval meter data (kWh)
BASELINE
10of10 | Firm Service Level (FSL)
Site-specific operational baseline | System benchmark
Average load during the 10 most recent comparable weekdays (or weekends), at the same hour | Based on MISO system peak conditions

## Slide 3
Portfolio Load Profiles

## Slide 4
Building Type Inference
Site | Likely Type | Daily Variability | Weekend Effect | Other Evidence
1 | Large Industrial(M-F) | Large hourly swings (5MW -> 20+MW) | Moderate | Lower and more stable weekend load. Likely energy-intensive manufacturing processes that spikes up the load.
2 | Mid-Sized Plants (M-F) | Low | Large | Weekday mean load ~ 5MW with low volatility; nearly shut down on weekends.
3 | Office/Institutional Buildings | Midday Peak | Minimal | Stable base load with low peak-base ratio (~1.6)
5 | 24/7 Commercial or hospital | Low, slight overnight trough | Minimal | Relatively stable load throughout; low peak-base ratio (~1.25)
6 | Small business-hour building | Daily Cycle, high usage 8am-9pm | None | Low average demand (~200kW).

## Slide 5
Event Response

## Slide 6
Site | 10of10 Avg (kW) | FSL Avg (kW) | Higher Baseline
Site 1 | 3937 | 3337 | 10of10
Site 2 | 4345 | 5075 | FSL
Site 3 | 649 | 850 | FSL
Site 5 | 3500 | 3235 | 10of10
Site 6 | -12 | 41 | FSL
Baseline methodology affects performance measured, and thus financial payout.
Different operational pattern benefit from different baselines:
  If the customer has been recently using high load, then the 10of10 baseline would increase, making their event reduction look larger.
Baseline Performance
Chart: Cross-Site Comparison: Average Curtailment Performance
| Site 1 | Site 2 | Site 3 | Site 5 | Site 6
10of10 Avg (kW) | 3937 | 4345 | 649 | 3500 | -12

## Slide 7
Site | Gross Revenue | Customer Payment | Voltus Profit
Site 1 | $24,217 | $15,499 | $8,718
Site 2 | $30,770 | $19,077 | $11,693
Site 3 | $4,600 | $2,576 | $2,024
Site 5 | $23,873 | $15,518 | $8,356
Site 6 | $71 | $36 | $35
Sum | $83,531 | $52,706 | $30,826
Revenue concentrated in Sites 1, 2, and 5.
Assumption: negative performance floored at 0.
Financial Results
Chart: 
| Site 1 | Site 2 | Site 3 | Site 5 | Site 6
Voltus Profit | 8718 | 11693 | 2024 | 8356 | 35

## Slide 8
Site 2 Deep Dive
Site 2 was the strongest performer. Event load dropped to ~320 kW against a ~4,700 kW baseline, meaning it curtailed over 90% of its normal usage.

## Slide 9
Hour | Load (kw) | 10of10 Baseline (kW) | 10of10 Performance (kW) | LMP ($/MWh) | Gross Rev | COGS | Profit
14:00 | 328 | 4,744 | 4,417 | 1,500 | $6,625 | $4,108 | $2,518
15:00 | 320 | 4,676 | 4,356 | 1,800 | $7,841 | $4,861 | $2,980
16:00 | 331 | 4,652 | 4,320 | 3,000 | $12,961 | $8,036 | $4,925
17:00 | 320 | 4,606 | 4,286 | 780 | $3,343 | $2,073 | $1,270
Total |  |  |  |  | $30,770 | $19,078 | $11,693
Chart: Site 2: Gross Revenue by Hour
| 0.58333333333333337 | 0.625 | 0.66666666666666663 | 0.70833333333333337
Gross Rev | 6625 | 7841 | 12961 | 3343
The 16:00 hour alone generated nearly $13K in gross revenue due to the $3,000/MWh LMP spike.

## Slide 10
Q: If given 500 CSVs?
Modular code with reusable functions.
Runtime scale almost linearly with number of sites.
Primary incremental effort: QA / validation
Optionally, parallelize computations for each site
Scalability & Discussion
Strength of the Analysis
Scalable for larger dataset; clear separation of logic
Parameter-driven config (no hard-coded values)
Clearly documented assumptions
Future improvement:
Integrate holiday calendar and exclude them in weekday baseline calculations.
Enhance ways to detect missing values/outliers/duplicates.
Better handle edge cases: multi-day dispatch event, discontinuous event windows, etc.